## Slide 1: BOSS: Building Operating System Services
Stephen Dawson-Haggerty, Andrew Krioukov, Jay Taneja, Sagar Karandikar, Gabe Fierro, Nikita Kitaev, and David Culler
Computer Science Division
University of California, Berkeley
© 2013 All rights reserved

## Slide 2
Sutardja-Dai Hall
UC Berkeley
93,000 sq. ft.
with Digital Controls
73% of US electricity is consumed in buildings
U.S. Energy Information Administration, 2009
2/3 of building occupants are uncomfortable
UC Berkeley CBE Study of 30,000 occupants
>70% of large buildings have digital controls

## Slide 3
151 Temperature Sensors
312 Light Relays
12 Variable Speed Fans
138 Air Dampers
50 Electrical Sub-meters
> 6,000 Sense and Control Points
Notes: Distributed networks with control over physical spaces

## Slide 4: Applications
Ventilation Optimization:
17% energy savings
Automated Fault Detection:
10 - 40% energy savings
Occupant Lighting Controls
50-60% savings

## Slide 5: Goals and Challenges
Portability
  Write once, run anywhere for buildings?
  Current practice: hand-coded logic
Fault tolerance
  Partial failures of controllers
  Network partitions
  Current practice: really tough hardware
Multiple processes
  Concurrent applications and users
  Current practice: none
Federation
  Multiple heterogeneous systems
  Current practice: lots of stovepipes
Scale
Security & privacy

## Slide 6: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface
Notes: HPL = Hardware Presentation Layer = sMAP
Decomposition onto hardware is important – the transaction manager needs to be in the building, for instance.

## Slide 7: Technologies in BOSS
Python
Some C for performance critical parts
RESTful
JSON
DNS naming for finding services
All data is within a shared global namespace
Propriety DB and Spatial DB
Approximate query language to select components
ETL for cleaning and filtering
Notes: ETL = Extract Transform

## Slide 8: Analytics side note
“Finally, there has previously been a separation between analytics, which deal with historical data, and control systems, which deal with real-time data. We demonstrate how to treat these uniformly in this environment, and present a time series service which allows applications to make identical use of both historical and real-time data.”

## Slide 9: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface
Elevates plethora of sensors and actuators to RESTful level
Places all data within global namespace.
Notes: HPL = Hardware Presentation Layer = sMAP
Decomposition onto hardware is important – the transaction manager needs to be in the building, for instance.

## Slide 10: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface
Semantic modeling to describe relationship between sensors, actuators, and equipment

## Slide 11: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface
Real-time access to all sensors, and
Historical data
Provides analytical operators for cleaning and processing data

## Slide 12: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface
Robust and safe interface for external processes
Provides all or nothing, recovery, roll-back
Defines fault domains

## Slide 13: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface
Notes: HPL = Hardware Presentation Layer = sMAP
Decomposition onto hardware is important – the transaction manager needs to be in the building, for instance.

## Slide 14: Hardware Presentation Layer (HPL)
Read and Write the point
Subscribe to changes
Receive periodic notifications about the value
Retrieve and Append metadata

## Slide 15: Hardware Presentation Layer (HPL)
sMAP hides complexity and diversity
Everything is a point
Points become time series (streams)
Buffering
Leasing
Discovery
  Key-value pairs describes the data
Aggregation

## Slide 16: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface

## Slide 17: Hardware Abstraction Layer (HAL)
Buildings are custom designed
Challenge: Portability
Notes: unique shape, layout, heating, ventilation, air conditioning, lighting and electrical system.

## Slide 18
Open area 450
Hardware Abstraction
Physical view
Notes: Personalized microclimate app

## Slide 19
VAV S4-21
Hardware Abstraction
Systems View
Notes: VAV = Variable Air Volume

## Slide 20
Hardware Abstraction
Controls view
SDH.MEC-08.S4-21:DMPR COMD
device: 220018 instance: 101
SDH.MEC-08.S4-21:VLV COMD
device: 220018 instance: 102
Controller
Air
Damper
Reheat coil
BACnet
Notes: The level at with existing application operate

## Slide 21
legacy solution: encode everything in point name
SDH.MEC-08.S5-01.AIR_VOLUME
building name
MEC: Modular Equipment Controller #8
S: VAV, 5: 5th floor, 01: the 1st one
quantity being measured

## Slide 22: Hardware Abstraction Layer (HAL)
Query language:
lights in room 410
Supports spatial queries
Uses graphs to describe Electrical distribution, HVAC mechanical interactions, and Lighting
Drivers in the HAL layer provide common methods:

## Slide 23: Hardware Abstraction Layer (HAL)
Drivers in the HAL layer provide common methods:
set_speed set_temperature implemented using control loops over HPL points

## Slide 24: Hardware Abstraction Layer
Program applications in terms of relationships between system components
  “it gets too hot on the sunny side”
Allow for scale by avoiding hard-coding
  “Run this in every room, except those on the north side”

## Slide 25: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface
Notes: Functional components, interfaces, concerns.
Also the decomposition onto hardware is important – the transaction manager needs to be in the building, for instance.

## Slide 26
BOSS solution: “transactions”: write access to the building
Writes to distributed resources
Which interact in physical space
Which are subject to failure
How to keep buildings safe despite app developers?
BOSS solution: Extend writes with
  Priorities
  Leases
  Notifications
  Reversion sequences

## Slide 27: Transaction
Coordinate writes across multiple points
During Lease time all actions are valid
Revert sequence How to undo action
Error policy What to do in partial failure

## Slide 28: BOSS: Building Operating System Services
HPL
HPL
Hardware Abstraction Layer
Auth.
Trans. mgr.
Time-series
Security
Abstraction
Isolation + Scheduling
HPL
HPL
Control processes
History
Fault tolerance
“Kernel” interface

## Slide 29: Authorization
Problem with building supervisors
General need for security
BOSS Solution
  only lights on the fourth floor
  cannot dim the lights below 50%
  access only provided at night
Checks on individual points and each method call
Two stage authorization process

## Slide 30: Future work
Control systems + CS future work
  Making use of the torrent of data?
  Compile/enforce constraints into the network?
  How to verify applications are behaving?

## Slide 31: Question and answers

## Slide 32: More BOSS
sMAP Hardware Presentation Layer
  30 Drivers, 30k data streams
Archiver data storage service
  500 writes/sec
  Stream cleaning and processing
Family of apps
  Personal ventilation and lighting control
  Electric grid-aware consumption
Name | Sensor Type | Access Method | Channels
ISO Data | CAISO, NYISO, PJM, MISO, ERCOT | Web scrape | 1211
ACme devices | Plug-load electric meter | Wireless 6lowpan mesh | 344
EECS submetering project | Dent Instruments PowerScout 18 electric meters | Modbus | 4644
EECS steam and condensate | Cadillac condensate; Central Station steam meter | Modbus/TCP | 13
UC Berkeley submetering feeds | ION 6200, Obvius Aquisuite; PSL pQube, Veris Industries E30 | Mosbus/Ethernet, HTTP | 4269
Sutardja Dai, Brower Hall BMS | Siemens Apogee BMS, Legrand WattStopper, Johnson Control BMS | BACnet/IP | 4064
UC Davis submetering feeds | Misc., Schneider Electric ION | OPC-DA | 34 (+)
Weather feeds | Vaisala WXT520 rooftop weather station; Wunderground | SDI-12, LabJack/Modbus, web scrape | 33
CBE PMP toolkit | Dust motes; New York Times BMS | CSV import; serial | 874

## Slide 34: Takeaways
Applying computer systems design to buildings: lots of pieces, potential
  Control systems
  Mechanical systems
  Occupants
30% electricity + steam savings, 60% lighting savings in test apps
Many pieces at http://smap.cs.berkeley.edu
Control systems + CS future work
  Making use of the torrent of data?
  Compile/enforce constraints into the network?
  How to verify applications are behaving?
Notes: A lot of the work on SDNs/constraint checking/policy enforcement seems relevant

## Slide 35
Write applications in terms of relationship between hardware elements

## Slide 36: BOSS
Hardware presentation layer: sMAP
Hardware abstraction layer: device-specific logic
Time-series service: the archiver
Reliable control inputs: the transaction manager
Security: the authorization service
a collection of services enabling portable, robust applications for the physical environment

## Slide 38
writer 1 value: 69F
69
writer 2 value: 73F
73
No arbitration between applications
Orphaned writes

## Slide 39: Command Sequence
Set damper to 100% open
Set valve to 0% open
… wait 10 minutes
Reset to “whatever was happening before”
What if…
#1 or #2 fail?
Client fails/becomes partitioned during #3?
Another application tries to do something?

## Slide 40
writer 1 value: 69F priority: 3 lease: 3600s
writer 2 value: 73F priority: 1 lease: 300s
69
73
present value: 69cfm
present value: 73cfm
<time passes>
writer 2 clear
BOSS solution: “transactions”
priority array
1
16
writer 1 crashes
Extend writes with
  Priorities
  Leases
  Notifications
  Reversion sequences
overridden!
… writer 1 revert sequence runs
71

## Slide 41: Hardware Abstraction Layer
#VAV > $(120, 20)
Notes: Capture Functional, spatial relationships
Driver instance, Objects, Domain
Names, tags