A Measurement Study of Interference Modeling and Scheduling in LPWN
Ritesh Maheshwari, Shweta Jain, Samir R. Das
Department of Computer Science
Stony Brook University

---
Outline
Interference Models
Experimental Platform
Measurement Approach
Results
Related Work
Future Work

---
Interference Models
Physical models (not pair-wise)
  - SINR: signal-to-interference-plus-noise-ratio
    - Threshold model (binary sense of interference)
    - Graded physical model (probability)
Pair-wise models
  - hop-based
  - range-based
  - protocol model
  - link quality-based

---
   Experimental Platform
TelosB motes using CC2420 radio
  - 802.15.4 compliant
  - Bit rate 250Kbits/s
  - 5MHz bandwidth in 2.4GHz ISM band
  - Frequency Channels: F(a) 2480MHz, F(b) 2479MHz, F(c)2478MHz (do not overlap with 802.11)
  - Power levels: -25(-32.5)~0dBm in 8 steps
  - Provides estimated RSS(received signal strength) in register over 32 bit periods(128μs)

---
MAC Layer & Measurement Process
TDMA
  - time synchronize with 'base station'
  - one-hop to other nodes
  - BS beacons (500ms interval)
  - multichannel multi-motes on BS
  - implementation of 32KHz precision timer
BS as command & control center for measurement process
  - broadcast 'command' to nodes
  - 'poll' to collect data

---
Indoor Test Bed
[Speaker Notes: Links show have at least 99% PRR(packet reception rate), topology for -32.5 dBm transmit power]

---
Outdoor testbed

---
Measurement Approach
Model Creation
  - 3 nodes to measure the model parameters
Validation for different transmit powers and channels
  - Validation for multiple interference for physical models
Evaluating Modeling Accuracy
  - Random sampling using random matchings
Evaluating Scheduling Performance
  - Greedy schedule algorithm
  - One-shot scheduling for the 2 physical models

---
Measurement Approach

---
Measurement Approach
Model Creation & Validation
Evaluating Modeling Accuracy
Evaluating Scheduling Performance

---
3 motes for model creation & validation
receiver--stationary
transmitter-- vary position
interferer—vary positions
various interference patterns at the receiver
  - d(sndr, rcvr): 1 to 64 feet
  - d(interfer, rcvr): 1 to 64 feet
packet size: 128 bytes

---
Physical Interference Models
BER->PER->1- PER->PRR for evaluation of interference
PRR vs. SINR
  - transition region
  - SINR threshold or capture threshold
  - Graded physical interference model
noise estimation
  - no transmission, RSS sampling of every 20ms for 6 seconds

---
Physical Interference Models
Pair-wise RSS measurement
  - transmitter and interferer take turn to send 1000 packets, each packet transmission time about 4ms
  - receiver sample each 3 ms of RSS
  - filter invalid sample with noise measured before
  - 8 power levels->64 experiments
  - calculate SINR
Concurrent transmission
  - concurrently transmit 1000 packets
  - measure PRR of receiver

---
Results-Single Interferer

---
Validation with Multiple Interferers
1 transmit power is used (-32.5dBm)
3~6 motes transmit concurrently
100 times random transmitter choosing
Other motes as receivers
Coefficient of determination values with respect to the fitted curve is always over 0.90

---
Multiple Interferers

---
Multiple Interferers with different transmit power and channels

---
Pair-wise Interference Models -- Notations
Network Graph G(V,E)
l(u,v): link between sender u and receiver v
d(u,v): distance
l(x,y): interference transmission to l(u,v)
Binary sense of interference
  - PRR on l(u,v)
    - 0 if l(x,y) interference
    - 1 otherwise

---
Pair-wise Interference Models
Hop-based model
  - interference if x within k hops of v , k = 1,2
Range-based model (disk model)
  - transmission range d(t), interference range d(i)
  - assume d(u,v) <= d(t)
  - interference if d(x,v) <= d(i)
  - does not consider capture effect

---
Pairwise Interference Models(cont.)
Protocol model
  - d(x,v) <= (1+Δ)d(u,v), Δ independent of d(u,v) and d(x,y)
Link quality-based model
  - using any concept of distance or SINR require pairwise distance or signal strength measurements
  - not feasible always
  - we use PRR to measure link quality
  - interference exists if l(x,v) has PRR more than a given interference threshold
  - assume: l(u,v) has high PRR larger than transmission threshold

---
Model Parameters

---
Measurement Approach
Model Creation & Validation
Evaluating Modeling Accuracy
Evaluating Scheduling Performance

---
Experimental design
Compare models for TDMA transmission scheduling, which determine feasible transmission sets (links) in each slot
Sampling of randomly chosen set of links
Measure the throughput of the set
Predicted throughput by interference model (conflicting links with 0 throughput)
Random matching: no 2 links have common end point
A heuristic to pick up random matchings
13,000 (indoor) random matchings and 3,000(outdoor), 1000 concurrent transmissions each

---
Results-Modeling Error(indoor)

---
Results-Modeling Error(indoor)

---
Results-Modeling Error(outdoor)

---
Results-Modeling Error(outdoor)

---
Measurement Approach
Model Creation & Validation
Evaluating Modeling Accuracy
Evaluating Scheduling Performance

---
Experiments Setup
Only indoor testbed
Greedy scheduling algorithm
  - 4 demand vectors on links f={f(1),...,f(|E|)}
  - links randomly split into 2 equal sets: 1 or i packets for vector i each link
  - schedule computation done by 'base station'
  - trials repeated 1000 times for each demand vector
  - performance: measured aggregate throughput in packets/slot
  - each slot 1 packet transmission and processing time in the mote (12.5ms)

---
Throughput for various models

---
One-shot scheduling for graded physical model
Picks a subset of S of links from a given set L such that the aggregate throughout is maximized
Throughput->expected throughput
Exhaustive search of S(opt) for small L, |L| <= 10
1024 possibilities
50 experiments of random L selection, each 5 times

---
One Shot Scheduling Experiment (indoor)

---
Conclusions
Physical models the best accuracy
  - Still 90-percentile error 20%~25%
Other Commonly used models poor accuracy
  - The best about 12~18 percentile points poorer
If pair-wise model must be used, avoid range-based(widely used) model, use protocol(outdoor) or hop-based(indoor)
Threshold physical model in scheduling
  - Conservative, not use links in transition region
Graded physical model recommended

---
Related Work
simulation using straightforward propagation and radio models
  - Physical model leads to more efficient schedules than protocol model
Effective of interference using experimental methods
  - transition region and its effects
  - multiple interferers
  - RSSI is good estimate of link quality
  - On 802.11-based systems

---
Future work
Measurement on other commodity radio platforms
CSMA as MAC model
Modeling link or path capacity for upper layer uses (routing) for different interference models

---
My Thinking
Will result test-bed specified?
Problem of using Physical model in scheduling algorithm
  - Determine SINR without real packet transmission

---
Q&A
Thanks!